## Slide 1
Faculty of Engineering Sciences
Dept. of Communication Systems Engineering
Smart Mesh Management & Peering
Maxim Altshul, Daniel Harari
Advisors: Prof. Michael Segal, Mr. Yaniv Machani
371-17-04
Simulation environment + Logger to test our algorithm
OS Dispatcher module to operate WiLink8 devices
What is Mesh?
Extension to the 802.11 protocol
Defines an architecture and protocol that supports multicast-broadcast-unicast by using radio-aware metrics over self-configuring multi-hop topologies
Project Motivation
      TI WiLink 8 wireless chip supports a max of 10
      connections
      Standard defines a random connection phase
        Disjoint, high-latency, low-throughput network might be formed
Erlang
Programming language chosen for implementation
Distributed, soft-real-time and fault tolerant
Communication between nodes using message passing
SW Design
Project’s Goal
Overcome the 10 connection limit
Control the Mesh connection phase
Construct a favorable mesh network
Network must have the lowest metric possible
TI’s Connection Algorithm
Each node “helps” it’s neighbors
Disconnects nodes that have other connections
Connects an “orphan” node
Repeat until the network is connected
A Connected graph is formed
GHS Algorithm
Created by Gallager-Humblet-Spira
Distributed MST algorithm
Creates a logical MST network backbone
Only the best connections are kept
Harari-Altshul Algorithm
Each node calculates un-direct metrics to it’s neighbors on the MST
The node will calculate the direct connection metric
The node calculates the best improvement: max(UndirectMetric – DirectMetric)
All nodes report to “Core” node, which decides who connects at the current phase
Algorithm repeats until all resources are used
SW Design
Results
Algorithm
Background